## Thiele Small Parameters

| Re | 6.7 Ohm |
| --- | --- |
| Le | 0.37 mH |
| Fs | 51 Hz |
| Qms | 2.0 |
| Qes | 0.66 |
| Qts | 0.49 |
| Sd | 129 cm ² |
| Vas | 18.5 L |
| Cms | 0.8 mm / N |
| Mms | 12 g |
| Rms | 2.0 kg / s |
| B * L | 6.3 N / A |
| Sensitivity 1 W / 1 m | 88.1 dB |
| Sensitivity 2.83 V / 1 m | 88.9 dB |

## Voice coil data

| Diameter | 25 mm |
| --- | --- |
| Height of winding | 9 mm |
| Support material | Aluminum |
| Coil material | Copper round wire |
| Air gap depth | 5 mm |
| linear excursion Xmax | 4 mm (peak to peak) |
| Outer diameter | 168 mm |
| Mounting diameter | 141 mm |
| Cutting depth, rim height | 4 mm |
| Depth | 66 mm |
| Nominal impedance | 8 Ohm |

## General data and characteristics

- Druckgußkorb black aluminum, very stable against steel basket

- 8 mm pole piece for voice coil ventilation

- Very high quality coated paper cone in black unpressed Paper Cone Design

- Inverted dust cap

- High quality butyl rubber surround for long life

- Large Ferritkernmagnetantrieb

- Gold plated solder tails

- Very high quality bonds